## Slide 1: Measurement Activities and Upgrades at Helmholtz Zentrum Berlin
E. Rial on Behalf of HZB Undulator Group
IMMW22 – CNPEM, Brazil – 30.09.2022
A Rich history of measurement

## Slide 2: HZB Undulator Group - Acknowledgement
Group Leadership
Theory
Operations & Measurement
Stefan Gottschlich
Michael Scheer
Stefan Schäfer
Paul Volz
Carsten Kuhn
Electrical Engineering
Christoph Rethfeldt
Simon Gaebel
Atoosa Meseck (Group Leader)
Ed Rial (Deputy)
Mechanical Engineering
Stefan Grimmer
Sebastian Knaack
Annette Rogosch-Opolka
Technician Support
Jürgen Bakos
Florian Laube
Mario Strehlke
Johannes Bahrdt (Project Support)

## Slide 3: IDs at HZB
1998
1999
1999
1998
1999
2000
2000
2001
2002
2002
2003
2004
2004
2006
2007
2007
2009
2010
2015
2017
2021
2023
UE51
UE56S
CU17
U49-1
UE56-2
UE56-1
U41
U49-2
U125-2
UE46
UE52
U139
UE49
UE112
UE48
CPMU17
U49-1
U125-1
UE56-1
UE56-2
U41
U49-2
U125-2
UE56
UE46
UE52
UE56 R
U139
UE49
UE112
U48
UE56 K
UE65
CU9
UE48

## Slide 4: Facilities - Overview

## Slide 5: Facilities - Schwerlasthalle
3D Zeiss CMM
Hall Probe Bench
Stretched Wire
Fixed Wire
Helmholtz Coils
Mechanical Assembly Area
NMR + Dipole

## Slide 6: Facilities – Testinghalle 1
In-Vacuum Hall Bench
In-Vacuum Stretched Wire
Development Lab

## Slide 7: Status Equipment 01.2019
Equipment | Hardware | Software
Hall Probe Measurement Bench | ANORAD Motion Control Agilent Voltmeter | PASCAL OS/2
Stretched Wire Bench | ANORAD Motion Control Agilent Voltmeter | PASCAL OS/2
Fixed Wire Bench | Berger Lahr (since 1996) Keithley Nanovoltmeter | PASCAL OS/2
Helmholtz Coils | SSB Antriebstechnik (<1996?) Agilent Voltmeter | PASCAL OS/2
In-Vacuum Hall Probe | Controls Techniques Digitax Agilent Voltmeter | Labview Windows
In-Vacuum Stretched Wire | Controls Techniques Digitax Agilent Voltmeter | Labview Windows

## Slide 8: U48 – February - June 2019
1MAGNETIC TUNING AND INSTALLATION MODIFICATIONS OF UNDULATOR U48 FOR THE DELHI LIGHT SOURCE (DLS), M. Tischer et al
IPAC2021, Campinas, SP, Brazil, doi:10.18429/JACoW-IPAC2021-WEPAB131

## Slide 9: Status Equipment 2019
Equipment | Hardware | Software
Hall Probe Measurement Bench | ANORAD Motion Control Agilent Voltmeter | PASCAL OS/2
Stretched Wire Bench | ANORAD Motion Control Agilent Voltmeter | PASCAL OS/2
Fixed Wire Bench | Berger Lahr (since 1996) Keithley Nanovoltmeter | PASCAL OS/2
Helmholtz Coils | SSB Antriebstechnik (<1996?) Agilent Voltmeter | PASCAL OS/2
In-Vacuum Hall Probe | Controls Techniques Digitax Agilent Voltmeter | Labview Windows
In-Vacuum Stretched Wire | Controls Techniques Digitax Agilent Voltmeter | Labview Windows
Obsolescence and
Technical Debt

## Slide 10: Granite Measurement Bench Upgrade
Welcome to the 21st Century
Component | Original | Replacement
PC | IBM | Dell PC
Operating System | OS/2 Warp | Windows
Motion controller | ANORAD | Control Techniques Digitax
Software | Borland PASCAL | Labview
    Weaknesses in the data storage, and analysis pipeline remain!

## Slide 11: Undulator Rochade – Castling IDs
1. A new UE51 in section 15 replaces of U49-2
2. U49-2 moves to section 5 and replaces UE56-2
3. UE56-2 – modules separated and refurbished
4. UE56-module 1 replaces old UE56 at Slicing
5. UE56-module 2 goes to SESAME
U49-2
UE56-2
UE56
UE51
UE56
HESEB
UE56
U49-2
UE56-2

## Slide 12: UE56-2 – August 2020

## Slide 13: UE56 SESAME –January 2022

## Slide 14: U49-2 – August 2022

## Slide 15: Shimming Cycle
Shim
Measure
Analyse
Predict
Apply
  Measure
        Single scan trajectories saved to individual files
        Metadata and Data saved separately
        Organised by Folder
        Not possible to integrate undulator motion
  Analyse
        Standalone analysis programme used
        126 line input text file
        Multiple data input files
          Expert users only!
          Prone to user error…
  Predict
        Standalone shim programme
          Virtual Shims, Iron-Shims, L-Shims, Magic Fingers
          ASCII Data input (Metadata free)
          ASCII Output (Metadata free)
  Apply
        Post-processing required to make outputs technician-readable
  Process is SLOW!

## Slide 16: Ambitions – (Cryogenic) In-Vacuum APPLE
  Cryo-APPLE2
    Cryogenic In-Vacuum APPLE Device
        4 mm minimum gap
        ~1m length
  IVUE321
    In-Vacuum APPLE-II Device
        6mm minimum gap
        3.5m length
  In-Vacuum Stretched Wire
        Integration of Pulsed Wire Measurement System
  In-Vacuum Hall Probe Bench
          Improved position feedback
          Length Extension
          Improved Vacuum Compatibility

## Slide 17: Measurement Process Issues
  A Title
    No communication between measurement system and measurement target.
        Not possible to automate overnight/long duration measurements with changing e.g. gap, shift, current.
        Dead time on the measurement system
        Make the measurement and target control systems communicate
    Analysis requiring separate software/people/PCs and high level expertise
        Analysis turnaround on the order of hours
        Dead time on the measurement system
        Refactor analysis code, simplify usability. Port to Python or create Python wrapper.
    (Badly) decentralised data storage – local drives, backup drives, poor network coverage, no data display standards (Proliferation of ROOT, Python, MatLab personalised tools)
        Difficult to track data from raw to analysed
        Difficult to compare measurements
        Introduce a Traceable Data Standard for measurements and allow easy step to step comparison
Opportunities

## Slide 18: Process Roadblocks
  Software Choices
      OLDER Measurement SYSTEMS
        Control program PASCAL
          In house expertise retired
          Limited support for modern data formats
      NEWer Measurement Systems
        Control Program Labview
          Not a data analysis package
          Proprietary
      Analysis/SHIM
        Analysis/Shim: FORTRAN/RATFOR
          Not a language for motion controllers
          Computationally fast
          Multiple system dependencies
            Not easily transferrable PC to PC
          High barrier to entry
            Requires Expert User
Main roadblocks are
  Data Format Choices
      Text ASCII
        Easily readable, open format
        Non-self-describing
        Not secure
          Files in folders easily accidentally ‘dragged’ to the wrong place
        Unlinked data and metadata
        Low density data format

## Slide 19: Process Options
Control Systems
  Labview
        In-Group Expertise
        Strong Real-Time Functionality
        Proprietary
          Patchy driver support
          Expensive
          Small User Base
        Generates strong opinions…
  EPICS
        Wider Support Base in and out of house
        UI tools, archiving, driver support
        Open Source
        Growing Python interface environment
          PyEPICS, Ophyd, Bluesky
        Easier integration with EPICS controlled motors on measurement target systems
          Undulators, Electromagnets
Data Format OPTIONS
  TDMS
        Hierarchical
        High Density
        Self Describing
        Python bindings
        Designed for Labview Systems
        National Instruments Proprietary Data Structure
  HDF5
        Hierarchical
        High Density
        Self Describing
        Python bindings
        Open Data Format

## Slide 20: Conclusions
Strategise
Plan
Resource
Execute
  Strategise
        Explore solution space
          Software
          Controls
          Data Storage
          Fail Fast Mentality
  Plan
        Desired Outcomes
        Timescales
        Costs
        Staff
  Resource
        Scientist/Engineer
        Motion Control Expert
        Structured Student Support
  Execute
        Assess programme against milestones.
        Continue to provide measurements during development.
        Report progress at IMMW23